## Slide 1: HPL-2.3
Rundown of each slide:
Each slide contains a different value either from my HPL.dat or run_hpl.slurm tested on archer2
Each slide contains a list of control variables
Each slide will show the job ID’s and all relevant information
Finally a graph to show how the independent variable effects the efficiency and computing time
All data can be found on the HPLResults spreadsheet

## Slide 2: Finding Maximum Safe N
Control | Values
CC | mpcii
Optimisation Flags | .-O3
safety cooeficient | 0.8
NB | 256
RoundTo | 100
ID | Nodes | Cores | Memory (B) | Max N | Rounded to NB | P | Q | Time (s) | GFLOPS | Joules (J) | Power (W) | Efficiency (GFLOPS/W)
11325287 | 1 | 128 | 2.56E+11 | 160000 | 153600 | 8 | 16 | 971.76 | 2486.2 | 496249 | 510.6703301 | 4.868502933
11325302 | 2 | 256 | 5.12E+11 | 226274.17 | 204800 | 16 | 16 | 1184.5 | 4834.7 | 1273235 | 1074.913466 | 4.497757405
11325334 | 3 | 384 | 7.68E+11 | 277128.1292 | 256000 | 16 | 24 | 1808.94 | 6183.1 | 2909451 | 1608.373412 | 3.84431871
11325340 | 4 | 512 | 1.024E+12 | 320000 | 307200 | 16 | 32 | 2135.08 | 9052.4 | 4542056 | 2127.346985 | 4.25525317
11341414 | 5 | 640 | 1.28E+12 | 357770.8764 | 332800 | 16 | 40 | 2236.67 | 10987 | 5899281 | 2637.528558 | 4.165642099
11342747 | 6 | 768 | 1.536E+12 | 391918.3588 | 384000 | 24 | 32 | 2893.93 | 13044 | 8972484 | 3100.449562 | 4.207131818
11342004 | 7 | 896 | 1.792E+12 | 423320.2098 | 409600 | 16 | 56 | 3108.28 | 14739 | 10591880 | 3407.633804 | 4.325288704
11325490 | 8 | 1024 | 2.048E+12 | 452548.34 | 435200 | 32 | 32 | 3197.1 | 17188 | 12737812 | 3984.17691 | 4.314065461
Chart: Time to solving HPL of max safe N
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 971.76 | 1184.5 | 1808.94 | 2135.08 | 2236.67 | 2893.93 | 3108.28 | 3197.1
Chart: Efficiency of each solving HPL of max safe N
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 4.8685 | 4.4978 | 3.8443 | 4.2553 | 4.1656 | 4.2071 | 4.3253 | 4.3141
Finding the maximum “safe” N, using 80% of each node’s memory, this value is rounded to the nearest 100 for clarity and NB (256) for optimisation
Graphs show that jobs are more efficient when using n^2 number of nodes

## Slide 3: Increasing N on 8 Nodes
Control | Values
CC | mpcii
Optimisation Flags | .-O3
taskpNode | 128
Nodes | 8
P | 32
Q | 32
ID | N | Time (s) | GFLOPS | Joules (J) | Power (W) | Efficiency (GFLOPS/W)
11352859 | 54500 | 18.16 | 5943.5 | 164018 | 9031.828194 | 0.658061676
11352867 | 108800 | 79.89 | 10748 | 392057 | 4907.460258 | 2.190134904
11352955 | 163200 | 234.97 | 12333 | 953049 | 4056.045453 | 3.040646399
11352904 | 217600 | 481.73 | 14259 | 1934087 | 4014.877629 | 3.551540375
11353012 | 272000 | 897.55 | 14947 | 3564007 | 3970.817225 | 3.764212542
11353051 | 326400 | 1446 | 16032 | 5850048 | 4045.676349 | 3.962749024
11353091 | 380800 | 2191.44 | 16799 | 8537146 | 3895.678641 | 4.312214007
11353112 | 435200 | 3164.05 | 17367 | 12601484 | 3982.706974 | 4.360602001
Chart: Size N against energy consumed
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 5943.5 | 10748 | 12333 | 14259 | 14947 | 16032 | 16799 | 17367
Chart: Size N against Efficiency
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0.65806 | 2.1901 | 3.0406 | 3.5515 | 3.7642 | 3.9627 | 4.3122 | 4.3606
Chart: size N against Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 18.16 | 79.89 | 234.97 | 481.73 | 897.55 | 1446 | 2191.44 | 3164.05
Testing the change in computing time and efficiency of 8 nodes on varying problem sizes
Efficiency dramatically increases with a higher N, probably due to more cores being able to be used at their full capacity
Expected increase in time taken, with efficiency and energy consumed eventually plateauing showing their max possible efficiency and energy consumed

## Slide 4: Increasing Nodes on a Fixed N
Control | Values
CC | mpcii
Optimisation Flags | .-O3
N | 153600
NB | 256
ID | Nodes | P | Q | Time (s) | GFLOPS | Joules (J) | Power (W) | Efficiency (GFLOPS/W)
11362784 | 1 | 8 | 16 | 966.26 | 2500.3 | 491137 | 508.2865895 | 4.919075284
11362839 | 2 | 16 | 16 | 550.43 | 4389.2 | 626352 | 1137.932162 | 3.857171935
11362930 | 3 | 16 | 24 | 393.06 | 6146.6 | 626864 | 1594.830306 | 3.854077752
11362986 | 4 | 16 | 32 | 329.51 | 7331.9 | 671766 | 2038.681679 | 3.596392745
11363005 | 5 | 16 | 40 | 269 | 8981.3 | 693838 | 2579.32342 | 3.482037161
11363061 | 6 | 16 | 48 | 232.81 | 10377 | 793493 | 3408.32868 | 3.044600734
11363082 | 7 | 16 | 56 | 204.99 | 11785 | 767211 | 3742.675252 | 3.148817144
11363414 | 8 | 16 | 64 | 181.39 | 13319 | 794380 | 4379.403495 | 3.041281767
 | Alternative P Q configurations |  |  |  |  |  |  | 
11363504 | 5 | 20 | 32 | 272.2 | 8875.5 | 715967 | 2630.297575 | 3.374333035
11363492 | 6 | 24 | 32 | 237.13 | 10189 | 726467 | 3063.581158 | 3.325846281
11363469 | 7 | 28 | 32 | 219.03 | 11030 | 820012 | 3743.834178 | 2.946177495
11363126 | 8 | 32 | 32 | 197.04 | 12261 | 866448 | 4397.320341 | 2.788289014
Chart: efficiency of n nodes when N = 153600
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 5 | 6 | 7 | 8
 | 4.9191 | 3.8572 | 3.8541 | 3.5964 | 3.482 | 3.0446 | 3.1488 | 3.0413 | 3.3743 | 3.3258 | 2.9462 | 2.7883
Testing how efficiency changes with the number of nodes on the same problem size
N = 153600, used as a max “safe” value for 1 node
Potential deviations in efficiency due to P and Q configurations
Orange line represents other potential P Q values

## Slide 5: Increasing Number of Tasks per Node
ID | ntasks | P | Q | Time (s) | GFLOPS | Joules (J) | Power (W) | Efficiency (GFLOPS/W)
11369603 | 128 | 32 | 32 | 199.44 | 12114 | 866620 | 4345.266747 | 2.787861069
11369684 | 64 | 16 | 32 | 325.99 | 7411.1 | 1025159 | 3144.755974 | 2.356653445
11369767 | 32 | 16 | 16 | 546.8 | 4418.3 | 1393433 | 2548.341258 | 1.733794477
11369846 | 16 | 8 | 16 | 946.62 | 2552.2 | 2199974 | 2324.030762 | 1.098178235
11369878 | 8 | 8 | 8 | 1433.86 | 1684.9 | 2958871 | 2063.570363 | 0.81649748
11369909 | 4 | 4 | 8 | 2641.94 | 914.46 | 5148630 | 1948.806559 | 0.469241032
11369925 | 2 | 4 | 4 | 5130.4 | 470.91 | 9736828 | 1897.869172 | 0.248125638
Chart: Efficiency for N Tasks Per Node
| 128 | 64 | 32 | 16 | 8 | 4 | 2
 | 2.7879 | 2.3567 | 1.7338 | 1.0982 | 0.8165 | 0.46924 | 0.24813
Control | Values
CC | mpcii
Optimisation Flags | .-O3
nodes | 8
N | 153600
NB | 256
Testing the effect of setting the number of tasks per node,
The maximum number of tasks per node tested here is 128 as there are 128 cores per node and increasing beyond can lead to oversubscription
Decreasing the tasks per node rapidly increased computing time and efficiency, the reduced power on each node did not compensate for the much larger run times

## Slide 6: Changing P Q Configuration
Control | Values
CC | mpcii
Optimisation Flags | .-O3
Nodes | 1
N | 153600
NB | 256
taskpNode | 128
ID | P | Q | (P, Q) | Time (s) | GFLOPS | Joules (J) | Power (W) | Efficiency (GFLOPS/W)
11349987 | 1 | 128 | (1, 128) | 431.36 | 1545.5 | 210089 | 487.0386684 | 3.173259333
11350891 | 2 | 64 | (2, 64) | 368.71 | 1808.1 | 179500 | 486.83247 | 3.714008641
11350942 | 4 | 32 | (4, 32) | 328.36 | 2030.4 | 173815 | 529.3427945 | 3.835699704
11350955 | 8 | 16 | (8, 16) | 298.12 | 2236.3 | 156963 | 526.5094593 | 4.24740707
11350976 | 16 | 8 | (16, 8) | 295.31 | 2257.6 | 153915 | 521.1980631 | 4.331558691
11351046 | 32 | 4 | (32, 4) | 318.27 | 2094.7 | 171721 | 539.5450404 | 3.882345019
11351068 | 64 | 2 | (64, 2) | 388.08 | 1717.9 | 196859 | 507.2639662 | 3.386599708
11351101 | 128 | 1 | (128, 1) | 550.1 | 1211.9 | 270135 | 491.0652609 | 2.467900087
Chart: Efficiency from P Q configurations
| (1, 128) | (2, 64) | (4, 32) | (8, 16) | (16, 8) | (32, 4) | (64, 2) | (128, 1)
 | 3.1733 | 3.714 | 3.8357 | 4.2474 | 4.3316 | 3.8823 | 3.3866 | 2.4679
Testing the distribution of P and Q
P * Q = Nodes * ntasksPerNode
Standard practices have P <= Q
Results contradict this with P = 16, Q = 16 having a shorter job time and higher efficiency

## Slide 7: Testing Optimisation Flags (mpicc, cc, O3)
Control | Values
Nodes | 8
N | 435200
NB | 256
P | 32
Q | 32
mpicc |  |  |  |  |  | 
ID | Attempt | Time (s) | GFLOPS | Energy (J) | Power (W) | Efficiency (GFLOPS/W)
11365475 | 1 | 199.68 | 12099 | 867624 | 4345.072115 | 2.784533761
 | 2 | 197.08 | 12258 | 838174 | 4252.963264 | 2.882225695
 | 3 | 198.08 | 12197 | 850236 | 4292.386914 | 2.841542536
 | 4 | 200.72 | 12036 | 837049 | 4170.232164 | 2.886170248
 | 5 | 199.35 | 12119 | 850710 | 4267.419112 | 2.839889798
 | 6 | 201.27 | 12004 | 831985 | 4133.676156 | 2.903952691
 | 7 | 197.32 | 12244 | 837944 | 4246.624772 | 2.883230956
 | 8 | 200.7 | 12038 | 843104 | 4200.81714 | 2.865632947
 | mean | 199.275 | 12124.38 | 844603.3 | 4238.648955 | 2.860897329
mpicc | O3 |  |  |  |  | 
ID | Attempt | Time (s) | GFLOPS | Energy (J) | Power (W) | Efficiency (GFLOPS/W)
11364879 | 1 | 198.04 | 12200 | 839840 | 4240.759443 | 2.876843208
 | 2 | 196.29 | 12308 | 849510 | 4327.83127 | 2.843918635
 | 3 | 197.9 | 12208 | 816678 | 4126.720566 | 2.958281232
 | 4 | 199.13 | 12133 | 826268 | 4149.389846 | 2.924044366
 | 5 | 198.25 | 12186 | 874736 | 4412.287516 | 2.761832713
 | 6 | 201.63 | 11982 | 854234 | 4236.641373 | 2.828183683
 | 7 | 199.26 | 12125 | 863957 | 4335.827562 | 2.796467301
 | 8 | 200.84 | 12029 | 919957 | 4580.546704 | 2.626105742
 | mean | 198.9175 | 12146.38 | 855647.5 | 4301.250535 | 2.82695961
Testing the effect of mpicc and cc as compiler wrappers, and the addition of O3
Only a slight decrease in time taken for jobs, but cc was quicker by 0.8 seconds
cc | O3 |  |  |  |  | 
ID | Attempt | Time (s) | GFLOPS | Energy (J) | Power (W) | Efficiency (GFLOPS/W)
11365216 | 1 | 196.45 | 12298 | 844769 | 4300.173072 | 2.859884892
 | 2 | 198 | 12202 | 850126 | 4293.565657 | 2.841926961
 | 3 | 199.91 | 12085 | 813445 | 4069.056075 | 2.969976274
 | 4 | 198.7 | 12159 | 882007 | 4438.887771 | 2.739199689
 | 5 | 196.69 | 12283 | 883139 | 4490.004576 | 2.735631956
 | 6 | 196.3 | 12307 | 841334 | 4285.960265 | 2.871468525
 | 7 | 198.69 | 12160 | 884382 | 4451.064472 | 2.731930772
 | 8 | 199.89 | 12086 | 868283 | 4343.804092 | 2.782353841
 | mean | 198.0788 | 12197.5 | 858435.6 | 4334.064497 | 2.816546614

## Slide 8: Testing Optimisation Flags (hfp3)
cc | O3 | hfp3 |  |  |  | 
ID | Attempt | Time (s) | GFLOPS | Energy (J) | Power (W) | Efficiency (GFLOPS/W)
11369198 | 1 | 199.32 | 12121 | 848533 | 4257.139274 | 2.847217162
 | 2 | 198.97 | 12142 | 866753 | 4356.199427 | 2.787292043
 | 3 | 197.81 | 12214 | 868970 | 4392.952834 | 2.780362199
 | 4 | 198.46 | 12174 | 836020 | 4212.536531 | 2.889945264
 | 5 | 200.41 | 12055 | 877000 | 4376.02914 | 2.754780559
 | 6 | 198.05 | 12199 | 846014 | 4271.719263 | 2.855758829
 | 7 | 200.3 | 12057 | 875970 | 4373.290065 | 2.756963252
 | 8 | 198.88 | 12148 | 866740 | 4358.10539 | 2.7874498
 | mean | 199.025 | 12138.75 | 860750 | 4324.74649 | 2.807471139
Chart: Efficiency for each Optimisation Layouts
| mpicc | mpicc_O3 | cc_O3 | mpicc_O3_hfp3 | cc_O3_hfp3
 | 2.8609 | 2.827 | 2.8165 | 2.7614 | 2.8075
Control | Values
Nodes | 8
N | 435200
NB | 256
P | 32
Q | 32
mpicc | O3 | hfp3 |  |  |  | mpicc_O3_hfp3
ID | Attempt | Time (s) | GFLOPS | Energy (J) | Power (W) | Efficiency (GFLOPS/W)
11368965 | 1 | 198.17 | 12192 | 832863 | 4202.770349 | 2.900943661
 | 2 | 197.52 | 12231 | 883233 | 4471.613001 | 2.735254593
 | 3 | 200.75 | 12035 | 852295 | 4245.554172 | 2.834730052
 | 4 | 201.83 | 11970 | 869365 | 4307.412179 | 2.778930714
 | 5 | 200.44 | 12054 | 896038 | 4470.355219 | 2.696430017
 | 6 | 192.14 | 12574 | 876305 | 4560.762985 | 2.756994836
 | 7 | 197.27 | 12247 | 877191 | 4446.651797 | 2.754207111
 | 8 | 199.36 | 12119 | 917400 | 4601.725522 | 2.633577327
 | mean | 198.435 | 12177.75 | 875586.3 | 4413.355653 | 2.761383539
Hfp3 decreased jobs time taken on mpicc by on average 0.25% and increased time on jobs on cc by 0.25%
There was little effect on the efficiency of jobs running on cc
Mpicc without O3 and hfp3 had the highest efficiency but the slowest run time
Overall, very little difference was made by changing compiler optimisation flags

## Slide 9: Conclusion
The most efficient hpl job:
Uses 2^n nodes
Uses the number of nodes that is closest to the maximum safe value for N for a number of nodes
Uses mpicc without –O3 and –hfp3 for a slight increase in efficiency
Uses a P Q configuration where P is almost equal to Q